# E.G.S.P  ENGINEERING COLLEGE, NAGAPATTINAM

DEPARTMENT OF MCA

UNIT TEST II EXAMINATIONS

SUBJECT    :	COMPUTER ORGANIZATION                              	CODE               : MC7101

BRANCH     : MCA							  	SEMESTER     : I

TIME            : 1 HOUR  30Mins						MAX. MARKS : 50

PART-A  									(5 X 2= 10)

(Answer all the questions)

- What is a combinational circuit?

It is a circuit made up of logic gates and accepts input and generates the output based on the

present input alone without regard to the previous input.

- How many don’t care inputs are there in a BCD adder?

6 don’t care conditions

- Compare encoder and decoder.

An encoder is a digital circuit performs the inverse operation of a decoder. An encoder has 2n input lines and n output lines.

A decoder is a combinational circuit that converts binary information from the n coded inputs to a maximum of 2n unique outputs.

- Show the logic diagram of a basic flip-flop circuit with NOR gates

- Differentiate state table and truth table.

State Table

The time sequence of inputs, outputs and flip flop states may be enumerated in a state table.

The state table consists of three sections labeled present state, next state and output.

The present state designates the state of the Flip Flops before the occurrence of a clock pulse.

The next state shows the states of Flip Flops after the application of a clock pulse.

The output section lists the values of the output variables during the present state.

Both the next state and output sections have two columns. One for x=0 and the other for x=1

Truth Table

It shows the relationship between input and output values

PART-B

(Answer all the questions)

6.a.i) Implement a full-adder with 2 half- adders and an OR-gate.   (8)

Half Adder

| A | B | Sum | Carry |
| --- | --- | --- | --- |
| 0 | 0 | 0 | 0 |
| 0 | 1 | 1 | 0 |
| 1 | 0 | 1 | 0 |
| 1 | 1 | 0 | 1 |

Full Adder

| A | B | Cin | Sum | Cout |
| --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 |
| 0 | 0 | 1 | 1 | 0 |
| 0 | 1 | 0 | 1 | 0 |
| 0 | 1 | 1 | 0 | 1 |
| 1 | 0 | 0 | 1 | 0 |
| 1 | 0 | 1 | 0 | 1 |
| 1 | 1 | 0 | 0 | 1 |
| 1 | 1 | 1 | 1 | 1 |

ii) Discuss about subtractors  in detail. (8)

Half subtractor

The half-subtractor is a combinational circuit which is used to perform subtraction of two bits. It has two inputs, X (minuend) and Y (subtrahend) and two outputs D (difference) and B (borrow).

### Truth table

The truth table for the half subtractor is given below.

| X | Y | B | D |
| --- | --- | --- | --- |
| 0 | 0 | 0 | 0 |
| 0 | 1 | 1 | 1 |
| 1 | 0 | 1 | 0 |
| 1 | 1 | 0 | 0 |

Full subtractor

As in the case of the addition using logic gates, a full subtractor is made by combining two half-subtractors and an additional OR-gate. A full subtractor has the borrow in capability (denoted as BORIN in the diagram below) and so allows cascading which results in the possibility of multi-bit subtraction. The circuit diagram for a full subtractor is given below.

Easy way to write truth table
D=X-Y-Z (don't bother about sign)
B = 1 If X<(Y+Z)

X	Y	 Z	 D	 B

0 	0	 0	 0	 0

0 	0	 1	 1	 1

0 	1	 0	 1	 1

0 	1	 1	 0	 1

1 	0	 0	 1	 0

1 	0 	 1	 0	 0

1 	1	 0	 0	 0

1 	1	 1	 1 	 1				OR

b.Design a combinational circuit for BCD-to-excess-3 code convertor. (16)

- A code converter is a circuit that makes the two systems compatible even though each uses a different binary code.

- To convert from binary code A to binary code B, the input lines must supply the bit combination of elements as specified by code A and the output lines must generate the corresponding bit combination of code B.

BCD-to-excess-3 code converter

- Each code uses four bits to represent a decimal digit

- Four input and four output variables are present

- A, B, C, D  => Input variables

- W,X,Y,Z    => Output variables

- 4 binary variables have 16 bit combinations, only 10 are listed in truth table, others are don’t care conditions.

TRUTH TABLE

| INPUT BCD | OUTPUT EXCESS – 3 CODE |
| --- | --- |
| A | B | C | D | w | x | y | z |
| 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 |
| 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 |
| 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 |
| 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1 |
| 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 |
| 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 |
| 0 | 1 | 1 | 1 | 1 | 0 | 1 | 0 |
| 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 |
| 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 |

- Draw maps for BCD to excess 3 code converter

Z =   D’    									Y= C’D’+CD

X=B’C+B’D+BC’D’		                W=A+BC+BD

7.a) Implement BCD-to-decimal decoder. (16)

| INPUT | OUTPUT |
| --- | --- |
| W | X | Y | Z | D0 | D1 | D2 | D3 | D4 | D5 | D6 | D7 | D8 | D9 |
| 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 |
| 1 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 |
| 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 |
| 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 |
| 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 |
| 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |

D0= w’x’y’z’		D1=w’x’y’z		D2=x’yz’	D3=x’yz		D4=xy’z’

D5=xy’z		D6=xyz’		D7=xyz	D8=wz’		D9=wz

OR

b) Explain flip-flops in detail. (16)

- The most common types of flip – flops are:

        - RS Flip flop

        - D Flip Flop

        - JK Flip Flop

        - T Flip Flop

RS Flip flop

- RS flip-flop consists of a basic NOR flip-flop and two AND gates.

- The outputs of the two AND gates remain at 0 as long as the clock pulse (or CP) is 0, regardless of the S and R input values.

- When the clock pulse goes to 1, information from the S and R inputs passes through to the basic flip-flop.

- With both S=1 and R=1, the occurrence of a clock pulse causes both outputs to momentarily go to 0.

- When the pulse is removed, the state of the flip-flop is indeterminate, ie., either state may result, depending on whether the set or reset input of the flip-flop remains a 1 longer than the transition to 0 at the end of the pulse.

D Flip-Flop

- The D flip-flop is a modification of the clocked SR flip-flop. The D input goes directly into the S input and the complement of the D input goes to the R input.

- The D input is sampled during the occurrence of a clock pulse.

- If it is 1, the flip-flop is switched to the set state (unless it was already set).

- If it is 0, the flip-flop switches to the clear state.

JK Flip-Flop

- A JK flip-flop is a refinement of the SR flip-flop in that the indeterminate state of the SR type is defined in the JK type.

- Inputs J and K behave like inputs S and R to set and clear the flip-flop (note that in a JK flip-flop, the letter J is for set and the letter K is for clear).

- When logic 1 inputs are applied to both J and K simultaneously, the flip-flop switches to its complement state, ie., if Q=1, it switches to Q=0 and vice versa.

- Output Q is ANDed with K and CP inputs so that the flip-flop is cleared during a clock pulse only if Q was previously 1. Similarly, ouput Q' is ANDed with J and CP inputs so that the flip-flop is set with a clock pulse only if Q' was previously 1.

- Note that because of the feedback connection in the JK flip-flop, a CP signal which remains a 1 (while J=K=1) after the outputs have been complemented once will cause repeated and continuous transitions of the outputs.

- To avoid this, the clock pulses must have a time duration less than the propagation delay through the flip-flop.

- The restriction on the pulse width can be eliminated with a master-slave or edge-triggered construction.

- The same reasoning also applies to the T flip-flop presented next.

T Flip-Flop

- The T flip-flop is a single input version of the JK flip-flop. As  the T flip-flop is obtained from the JK type if both inputs are tied together. The output of the T flip-flop "toggles" with each clock pulse

8.a) Design a 3-bit binary counter that counts with the following binary sequence:

0,1,2,3,4,5,6,7   and repeat. Use T flip-flops. (8)

Characteristics Table

Output States Inputs Required

| Q | Q+1 | T |
| --- | --- | --- |
| 0 | 0 | 0 |
| 0 | 1 | 1 |
| 1 | 0 | 1 |
| 1 | 1 | 0 |

State Diagram

Truth Table

| INPUT | OUTPUT |
| --- | --- |
| X | Y | Z | Tx | Ty | Tz |
| 0 | 0 | 0 | 0 | 0 | 1 |
| 0 | 0 | 1 | 0 | 1 | 1 |
| 0 | 1 | 0 | 0 | 0 | 1 |
| 0 | 1 | 1 | 1 | 1 | 1 |
| 1 | 0 | 0 | 0 | 0 | 1 |
| 1 | 0 | 1 | 0 | 1 | 1 |
| 1 | 1 | 0 | 0 | 0 | 1 |
| 1 | 1 | 1 | 0 | 1 | 1 |

Construct the K- Map

Draw the appropriate logic diagram

OR

b) Explain about state reduction and assignment. (8)

- The information available in a state table may be represented graphically in a state diagram.

- Here, a State is represented by a Circle

- Transition between states is indicated by directed lines connecting the circles.

- The binary number inside each circle identifies the state the circle represents.

- The directed lines are labeled with two binary numbers separated by a /.

- The input value that causes the state transition is labeled first.

- The number after the symbol / gives the value of the output during the present state.

- For example, the directed line from state 00 to 01 is labeled 1/0, meaning that the sequential circuit is in a present state 00 while x=1 and y=0, and that on the termination of the next clock pulse, the circuit goes to next state 01.

- A directed line connecting a circle with itself indicates that no change of state occurs.

- The state diagram provides the same information as the state table and is obtained directly from the table

- There is no difference between a state table and a state diagram except in the manner of representation. The state table is derived from the logic diagram and then followed by a state table.

STATE REDUCTION AND ASSIGNMENT

- The analysis of sequential circuits starts from a circuit diagram and culminates in a state table or diagram.

- The design of a sequential circuit starts from a set of specifications and culminates in a logic diagram.

- STATE REDUCTION

- Any design process must consider the problem of minimizing the cost of the final circuit.

- The two most obvious cost reductions are reductions in the number of flip flops and the number of gates.

- State reduction algorithms are concerned with procedures for reducing the number of states in a state table while keeping the external input – output requirements unchanged.

- Since m flip flops produce 2m states, a reduction in the number of states may result in a reduction in number of flip flops.

- An unpredictable effect in reducing the number of flip flops is that sometimes the equivalent circuit may require more combinational gates.

- The reduction of the number of flip flops in a sequential circuit is referred to as the state reduction problem.

- Input Sequence : 01010110100 starting from the initial state a.

- Each input of 0 or 1 produces an output of 0 or 1 and causes the circuit to go to the next state.

- From the state diagram we obtain the output and the state sequence for the given input sequence as follows

- With the circuit in initial state a, an input of 0 produces an output of 0 and the circuit remains in state a.

- With present state a and input of 1, the output is 0 and the next state is b.

- With present state b and input of 0, the output is 0 and the next state is c.

- Continuing this process, we find the complete sequence to be as follows:

| State | a | a | b | c | d | e | f | f | g | f | g | a |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Input | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 |  |
| output | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 |  |

- The problem of state reduction is to find ways of reducing the number of states in a sequential circuit without altering the input output relationships.

| Present State | Next State | Output |
| --- | --- | --- |
|  | X=0 | X=1 | X=0 | X=1 |
| a | a | b | 0 | 0 |
| b | c | d | 0 | 0 |
| c | a | d | 0 | 0 |
| d | e | f | 0 | 1 |
| e | a | f | 0 | 1 |
| f | g | f | 0 | 1 |
| g | a | f | 0 | 1 |

- When two states are equivalent, one of them can be removed without altering the input output relationship

- From the above table, states e and g are equivalent, they both go to states a and f and have outputs of 0 and 1 for x=0 and x=1.

- Therefore, states g and e are equivalent, one can be removed.

- The row with present state g is crossed out and stage g is replaced by state e each time it occurs in the next state columnsReducing the State Table

| Present state | Next state | Output |
| --- | --- | --- |
|  | X=0 | X=1 | X=0 | X=1 |
| a | a | b | 0 | 0 |
| b | c | d | 0 | 0 |
| c | a | d | 0 | 0 |
| d | e | f d | 0 | 1 |
| e | a | f d | 0 | 1 |
| f | g e | f | 0 | 1 |
| g | a | f | 0 | 1 |

- Present state f now has next states e and f and outputs 0 and 1 for x=0 and x=1, respectively.

- The same next states and outputs appear in the row with present state d.

- Therefore states f and d are equivalent.

- State f can be removed and replaced by d.

- Draw the reduced state diagram with respective with the new reduced table.

# Text boxes

Z

Y

X

W

D

C

B

A

111

110

101

010

011

100

00101

0000