PART-A  (5 X 2= 10)

- Convert  (153.513)10 to octal.

0.513 x 8 = 4

0.104 x 8 = 0

0.832 x 8 = 6

0.656 x 8 = 5

0.248 x 8 = 1

(153.513)10  = ( 231.40651 )8

2. Simplify the following Boolean functions to a minimum number of literals:

a) (x+y) (x+y’)

= xx + xy’ + xy + yy’

= x + xy’ + xy [ since xx = x & yy’ = 0]

= x + x(y’ + y)

= x + x

= x

b) y(wz’ + wz) + xy

= yw(z’+z) + xy

= yw + xy [ since z + z’=1]

- Why NAND & NOR are called universal gates?

Basic logic gates are AND, OR & NOT. Since any basic logic gates can be constructed using NAND & NOR gates, they are called as universal gates.

- Give the advantages & disadvantages of K-map

Advantages:

  - It is used to simplify Boolean functions, hence useful to reduce the no. of gates involved in designing the circuit.

  - K map useful to simplify B.F up to 6 variables.

Disadv:

- No procedure is defined in grouping the minterms

- Useful only up to six variables

- Draw the logical diagram for the following Boolean expressions

i)F=x’y+xy’

ii F=xy+x’y’

PART-B

6.a) Simplify the Boolean function F together with the don’t care conditions  		(16)

F(W,X,Y,Z) = ∑ (0,1,2,3,7,8,10)

D(W, X,Y,Z) = ∑ (5,6,11,15)

F =    zw’+z ‘x’

(OR)

b. i) Write a short note on various logic gates with diagram                        	            (8)

ii) Simplify the following Boolean functions to a minimum number of literals:

a) x’y’+xy+x’y   	= x’(y’+y) + xy

= x’+ xy

b) (x+y)(x+y)’	=  0						(4+4)

7. a) Perform subtraction with the following unsigned decimal numbers by taking the 10’s

complement of the subtrahend

i) 5250-1321    ii) 1753-8640   iii) 20-100  iv) 1200-250                (4 x 4)

i) 5250 – 1321

10’s compl. 0f 1321

9999

1321

______

8678

+1

______

8679

Add 5250 with 10’s complement of 1321

5250+

8679

_____

3929

____

ii)1753 - 8640

10’s compl. 0f 8640

9999

8640

______

1359

+1

______

1360

Add 1753 with 10’s complement of 8640

1753+

1360

_____

3113

____

Since there is no carry take the 10’s complement of the solution and put minus sign  = -- 6887

iii) 20-100

10’s compl. 0f 100

999

100

______

899

+1

______

900

Add 20 with 10’s complement of 100

020+

900

_____

920

____

Since there is no carry take the 10’s complement of the solution and put minus sign

999

920

___

079+

1

___

-- 080

___

iv) 1200-250

10’s compl. 0f 250

9999

0250

______

9749

+1

______

9750

Add 1200 with 10’s complement of  250

1200+

9750

_____

1)0950 -> hence there is a carry, ignore the carry.

____

(OR)

b) i) Write the difference between AND & NAND gates and also write the implementation

concept of  NAND gate

Ans:

- AND: logic gate generates logic-1 as output if both the inputs are one.     -- 3

- Symbol

- Truth table:

| x | y | F |
| --- | --- | --- |
| 0 | 0 | 0 |
| 0 | 1 | 0 |
| 1 | 0 | 0 |
| 1 | 1 | 1 |

- NAND: logic gate generates logic-0 as output if both the inputs are one.     --3

- Symbol

- Truth table:

| x | y | F=(x.y)’ |
| --- | --- | --- |
| 0 | 0 | 1 |
| 0 | 1 | 1 |
| 1 | 0 | 1 |
| 1 | 1 | 0 |

- NAND implementation of AND  -- 2

(8)

ii) Implement the following using NOR gates:    F = AC’+B’D+A’CD+ABCD    (8)

Draw the appropriate logic gate diagram

8.a) Find the complement of F = x+yz ; show that FF’ = 0 and F + F’ = 1                       (8)

| X | y | z | yz | F=x+yz | F’ | FF’ | F+F’ |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 |
| 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 |
| 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 |
| 1 | 0 | 1 | 0 | 1 | 0 | 0 | 1 |
| 1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 |
| 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 |

Since as per the TT FF’ = 0 and F+F’ = 1 , hence proved.

(OR)

b) Write a note on a) Error detection code   b) Gray Code                         	          (8)

Error-Detection Codes

􀂾 Binary information may be transmitted through some communication medium, e.g. using wires or wireless media.

􀂾 A corrupted bit will have its value changed from 0 to 1 or vice versa.

􀂾 To be able to detect errors at the receiver end, the sender sends an extra bit (parity bit) with the original binary message.

􀂾

A parity bit is an extra bit included with the n-bit binary message to make the total number of 1’s in this message (including the parity bit) either odd or even. 􀂾 If the parity bit makes the total number of 1’s an odd (even) number, it is called odd (even) Parity 􀂾 The table shows the required odd (even) parity for a 3-bit message.

At the receiver end, an error is detected if the message does not match have the proper parity (odd/even).

􀂾 Parity bits can detect the occurrence 1, 3, 5 or any odd number of errors in the transmitted message.

No error is detectable if the transmitted message has 2 bits in error since the total number of 1’s will remain even (or odd) as in the original message. In general, a transmitted message with even number of errors cannot be detected by the parity bit.

Error-Detection Codes

􀂾 Binary information may be transmitted through some communication medium, e.g. using wires or wireless media.

􀂾 Noise in the transmission medium may cause the transmitted binary message to be corrupted by changing a bit from 0 to 1 or vice versa.

􀂾 To be able to detect errors at the receiver end, the sender sends an extra bit (parity bit).

Gray Code

􀂾 The Gray code consist of 16 4-bit code words to represent the decimal Numbers 0 to 15.

􀂾 For Gray code, successive code words differ by only one bit from one to the next as shown in the table and further illustrated in the Figure.